## Slide 1
45°
SMA female panel mount
Ground plane wires
Monopole
~90mm
~100mm
SIDE PROFILE
TOP PROFILE
12.5 mm
12.5 mm

## Slide 2
CONNECTION
SMA female panel mount
SMA female
SMA male
RG316
To NanoVNA or transceiver

## Slide 3: Notes
Build the monopole and ground wires to be 90/100mm long initially and then trim using NanoVNA to tune
Ground wires will be two wires with each end extending beyond the mount to make 4 radials. Total length to cut initially: 100 x 2 + 12.5 = ~215mm
Use SMA male to male for connection